## Slide 1: Resilience Bounds of Sensing-Based Network Clock Synchronization
Rui Tan Linshan Jiang Arvind Easwaran Jothi Prasanna Shanmuga Sundaram
School of Computer Science and Engineering
Nanyang Technological University
The 24th IEEE International Conference on Parallel and Distributed Systems (ICPADS)
December 11, 2018, Sentosa, Singapore.

## Slide 2: Outline
Background A bit long …
Problem Definition
Analysis & Results
Conclusion

## Slide 3: Clock Synchronization
Industrial systems need accurate clock sync
  ms or even μs accuracy
Desynchronization
  Degrade system performance
  Cause infrastructure damage
Roboteam
Notes: Now, I will present a recent work on using physical fingerprints for secure clock synchronization. Clock synchronization is a very basic system function. For example, many industrial systems such as power grids and manufacturing systems need accurate clock synchronization up to millisecond or even microsecond accuracy. The desynchronization will degrade system performance and even cause infrastructure damage. For example, this video shows a roboteam in a manufacturing system. We can see that they are highly coordinated. This coordination is driven by their synchronized clocks. If they are desynchronized, these robotic arms will clash with each other, causing equipment damages.

## Slide 4: Clock Sync Security
GPS
  Not scalable, vulnerable to wireless spoofing
Message exchange based protocols (NTP, PTP, …)
  Vulnerable to packet delay attack [RFC 7384] Implemented in wired/wireless networks
  No pure cryptographic solution
slave
master
t1
clock
clock
t2
t3
t4
t4’
Symmetric link assumption
Notes: GPS and various protocols are two major approaches to clock synchronization.
GPS can provide accurate time information. However, using GPS is not scalable and it does not work in indoor environment. And it is susceptible to wireless spoofing attacks.
NTP and PTP are examples of clock sync protocols. NTP is widely used in Internet and PTP is often used in mission-critical systems. Most protocols are based on this two-way communication principle. Specifically, the slave will record its clock values when it transmits the request and receives the reply. The master node also record its clock values when it receives the transmits the two packets. Then, based on an assumption that the two one-way transmission delays are the same, we can compute the clock offset between the slave and master nodes. And this offset is further used to update the clock of the slave. However, this principle is vulnerable to a simple but basic packet delay attack that breaks the symmetric link assumption. For example, if the attacker can delay the reply packet for a certain time duration, then the introduced error to the clock offset computation is half of the introduced delay. And this vulnerability has no pure cryptographic solution.

## Slide 5: Secure Sensing-Based Clock Sync
Common periodic impulses from physical ambient
  Synchronous: Impulses occur at the same time
  Securely synchronizable: Correspondence between two impulses w/o measuring network delays
slave
master
clock
clock
T

## Slide 6: Electric Network Voltage (ENV)
Synchronous
  100 μs offset over 10 km
Hard to compromise
  Inject large energy to distort 50Hz ENV
  Modify power network
Securely synchronizable?
?
Notes: To address the packet delay attack, we leverage the electric network voltage signal. We know that all power grids are alternating current power grids, and the voltage is a sine wave. Moreover, from power engineering, the voltage signals at different locations in an area, for example, a building or even up to a city, are highly synchronized. This figure illustrates the voltage signals at two locations with a phase shift. From our measurements in Singapore, this phase shift is just 0.2ms over 10 km distance. Moreover, power grid voltage is hard to compromise, unless the attacker launches physical attacks against the power grid infrastructures.

## Slide 7: Time Fingerprint (TiF)
TiF: a sequence of cycle lengths
  TiF form fluctuates randomly
  Nodes in an area observe similar forms
T
Notes: In this work, we explore a time fingerprint from the power grid voltage. We measure the cycle length of the voltage signal, which is illustrated in the top figure. A time fingerprint is a series of consecutive cycle lengths. The bottom left figure shows the traces of the cycle lengths captured by two nodes at two different places, and the right figure shows a zoom-in version. We can see that the fluctuations are kind of random and the fluctuations experienced by the two nodes are almost the same. So, we make two assumptions: first, we assume that the signal form does not repeat over a certain time period; second, nodes in an area observe similar signal forms. If the first is true, the signal form self-explains when the signal is captured; if the second is true, we can use it to synchronize two nodes, just by matching their signals. In fact, these two assumptions stem from a key property of power grid frequency – the power grid frequency is a random process, although it is regulated at 50Hz in Singapore for example, and the frequencies at any two locations in a power grid are very similar at the same time instant. Later, we will verify these two assumptions by measurements.

## Slide 8: Secure Sync via TiF Matching
Node A’s clock time
voltage cycle length
Node A’s TiF trace
Timestamp of Node B’s TiF
in terms of Node A’s clock
Rare matching errors
  With sufficiently long TiF, empirical prob. = 1
  Resulting sync error is nT

## Slide 9: Our Previous Studies
Wireless IoT sensors
Grid-connected devices
Time-critical wearables
S. Viswanathan, R. Tan, D. Yau, Exploiting Power Grid for Accurate and Secure Clock Synchronization in Industrial IoT, RTSS’16.
S. Viswanathan, R. Tan, D. Yau, Exploiting Electrical Grid for Accurate and Secure Clock Synchronization, ACM TOSN, Jul 2018.
Y. Li, R. Tan, D. Yau, Natural Timestamping Using Powerline Electromagnetic Radiation, IPSN’17 (best paper).
Y. Li, R. Tan, D. Yau, Natural Timestamps in Powerline Electromagnetic Radiation, ACM TOSN, Jul 2018.
Z. Yan, Y. Li, R. Tan, J. Huang, Application-Layer Clock Synchronization for Wearables Using Skin Electric Potentials Induced by Powerline Radiation, SenSys’17.
Z. Yan, R. Tan, Y. Li, J. Huang, Wearables Clock Synchronization Using Skin Electric Potentials, IEEE TMC, in press.
Clock sync insecurity caused by delay attack
Non-malicious matching errors

## Slide 10: Outline
Background
Problem Definition
Analysis & Results
Conclusion

## Slide 11: Network Clock Sync Model
n0
n1
n2
n3
A P2P clock
sync session
Constant clock offset between ni and nj
P2P clock sync may be faulty
Clock offsets estimation equation system
with sync faults considered
if the sync between ni and nj is faulty
otherwise
N-node system

## Slide 12: Sync Fault vs. Byzantine Clock Fault
Byzantine faulty clock [Lamport et al. in 1980s]
  A faulty clock always gives an arbitrary clock value whenever being read
  In a (3m+1)-node system with m faulty clocks, non-faulty clocks can remain synchronized
In this work, a node involved in a faulty sync session is not a Byzantine faulty clock
n0
n1
n2
n3
n0
n1
n2
n3
Byzantine clock fault
Sync fault

## Slide 13: Fault-Tolerant Network Clock Sync
Algorithm 1: Faulty-tolerant network clock sync algorithm
Given: All P2P clock offset measurements Output: Estimated P2P clock offsets and sync faults 1: for k = 0 to k = N(N-1)/2 do 2: for each distribution of the k assumed P2P sync faults among the N(N-1)/2 P2P sync sessions do 3: if the corresponding equation system has a solution then 4: return the estimated clock offsets and sync faults 5: end if 6: end for 7: end for
Requires neither the # nor the distribution of the actual P2P sync faults
How many sync faults Algorithm 1 can tolerate?
n0
n1
n2
n3
A 4-node system with a distribution of the k=2 assumed sync faults
Discrete sync errors enable this

## Slide 14: Q-Resilience
A N-node system is Q-resilient if Algorithm 1 can correct any Q P2P sync faults.
Q-resilience condition
  For any k ∈ [0, Q), the equation system with any distribution of the Q actual faults (dQ) and any distribution of the k assumed faults (dk) has no solutions;
  When k = Q, for any dQ and any dk
    If dQ = dk, the equation system has a unique solution*
    Otherwise, the equation system has no solutions.
* This unique solution must be correct.

## Slide 15: Resilience Bounds
fl(N) is a lower bound of the maximum resilience if any N-node network with Algorithm 1 is Q-resilient for Q ≤ fl(N).
fu(N) is an upper bound of the maximum resilience if any N-node network with Algorithm 1 is not Q-resilient for Q > fu(N).

## Slide 16: Outline
Background
Problem Definition
Analysis & Results
Conclusion

## Slide 17: Analysis Approach
The equation system used for estimating clock offsets and sync faults
The equation system used for analyzing Q-resilience

## Slide 18: Resilience of Certain Cases
n0
n1
n2
n3
n0
n1
n2
n0
n1
n2
n3
n3
N = 3
N = 4
N = 5
Not 1-resilient
1-resilient
Not 2-resilient
1-resilient
Not 2-resilient
Results for general N-node systems?
By enumerating counterexamples:

## Slide 19: Main Challenge and Approach
Values of actual sync faults matter!
  E.g., when k < Q, if actual sync faults satisfy certain condition, equation system may have (wrong) solutions
  A pitfall in analyzing the general Q-resilience
The equation system used for analyzing Q-resilience for general N-node system
Consider actual sync faults as unknowns

## Slide 20: Algorithm to Compute Lower Bound
Algorithm 2: Compute a lower bound of maximum resilience
Given: The number of nodes N Output: A lower bound of maximum resilience 1: for Q = 1 to Q = (N – 2) do 2: for each distribution of the Q actual P2P sync faults among the N(N-1)/2 P2P sync sessions do 3: for k = 0 to k = Q do 4: for each distribution of the k assumed faults among the N(N-1)/2 P2P sync sessions do 5: determine the value of l (i.e., the number of correctly positioned estimated faults) 6: if rank(A’) ≠ N – 1 + k + Q – l then 7: return Q – 1 8: end if 9: end for 10: end for 11: end for 12: end for
Refer to paper for the proof on why this algorithm computes a lower bound

## Slide 21: Resilience Bounds
(N – 2) is an upper bound of maximum resilience
  Any N-node system is not Q-resilient if Q > (N – 2)
N | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
fl(N) | 1 | 1 | 2 | 2 | 2 | 3 | 4 | 5 | 5
Computed lower bound of maximum resilience
  Any N-node system is Q-resilient if Q ≤ fl(N)

## Slide 22: Conclusion & Future Work
Analyzed resilience of sensing-based network clock sync
  An algorithm to compute a lower bound
  An analytical upper bound
Future work
  Tight bound
  Reduce # of P2P sync sessions